## Slide 1: Dymanic switch fabric power management using ML – logistic regression.

## Slide 2: Traffic variation at core routers (Reference - www.mdpi.com/1996-1073/9/10/837/pdf.)
Chart: Daily Traffic variation in Tbps
| 0.0 | 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0
Bandwidth | 2 | 2 | 2 | 2 | 2 | 2 | 4 | 6 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 6 | 4 | 2 | 2 | 2
Column1
Column2

## Slide 3: Power savings strategy:
According to Research studies done, traffic variations in the core routers are in bell shape – daily variation.
There are also seasonal variation – like vacation, festivals etc.
So Router may not need to function at line(Full) rate always.
A suitable Machine learning (ML)algorithm can be used to learn the traffic variation and predict BW requirement.
ML algorithm like logistic regression can be used to predict and classify as peak BW or low BW from input traffic.
May be applied to all ASICs in datapath with suitable damping.

## Slide 4: Prototype- details
Fabric plane 0 to 5 is chosen to power off
Single chassis NCS6k has 8Tbps BW and around 10Tbps full fabric BW
Input traffic rate of 5Tbps is taken as threshold
Below which causes low-BW level (<5Tbps)
above or equals high-BW level(>=5Tbps)
Input data rates from all interfaces are sampled at 1 ms and preprocessed.
ML algorithm is called every 1 ms – logistic regression predicts low-BW or high-BW , Based on this we can put fabric planes(ASIC groups) in low power mode via giving command to the SFE driver.
SFE driver puts the ASICs to sleep(powers off)/resumes on 2 fabric planes to save power